ECE 232

# Lab4

Second Order Circuits-2

Preliminary Work:

- Consider the RLC circuit of Fig.1.

C = 0.1µF

R1=10K Ohms.

L = 0.1 H

R = 100K Ohms Pot.

Vin(t) =Vpeak. u(t) volts

Fig. 1

  - Show that the differential equation for Vc(t) is;

  - Find the characteristic equation for the differential equation found on part a.

  - Find the resonance frequency of the circuit both in radians and in Hz.

Lab Work:

  - When the roots of the characteristic equation are repeated the response is called critically damped. Determine the value of the resistor R=R0 for the critically damped response.

  - Arrange potentiometer to R0 and Vin(t) is a 2 Vp-p square wave with 150Hz frequency plot Vin(t) vs. Vc(t) bellow.

  - Arrange R>R0 to observe overdamped response plot Vin(t) vs. Vc(t) bellow.

  - Arrange R<R0 to observe underdamped response plot Vin(t) vs. Vc(t) bellow.

    - For R=R0/2

    - For R=R0/4