ECE 232

# Lab4

Second Order Circuits-3

Preliminary Work:

- Consider the parallel RLC circuit of Fig.1.

R1 = 10 KΩ , R2 = 10 KΩ, C = 0.1 μF, L = 0.1 H

Fig. 1

  - Find the differential equation for Vc(t),

  - Find the characteristic equation for the differential equation found on part a.

  - Find the resonance frequency of the circuit both in radians and in Hz.

Lab Work:

  - When the roots of the characteristic equation are repeated the response is called critically damped. Determine the value of the resistor R=R0 for the critically damped response.

  - Arrange potentiometer to R0 and Vin(t) is a 2 Vp-p square wave with 150Hz frequency plot Vin(t) vs. Vc(t) bellow.

  - Arrange R>R0  to observe overdamped response plot Vin(t) vs. Vc(t) bellow.

  - Arrange R<R0 to observe underdamped response plot Vin(t) vs. Vc(t) bellow.

    - For R=R0/2

    - For R=R0/4